## Slide 1: Solar Energy Development in Six Southwestern States
Cathy Becker
Brinda Bhatt
Makenna Dunlap
Hannah Sargel
Stacey Silverii
Mikhail Yakhnitskiy

## Slide 2: Programmatic EIS
Lead agencies
  Bureau of Land Management
  Department of Energy
States
  Arizona
  California
  Colorado
  Nevada
  New Mexico
  Utah
BLM administers 120 million acres in these six states

## Slide 3: Project Description and Need
Great interest in developing utility-scale solar energy facilities on BLM-administered land
  127 active applications as of February 2010
Legislation
  Section 211 of Energy Policy Act of 2005
  Executive Order 13212
    Actions to Expedite Energy-Related Projects
    Signed by George W. Bush on May 18, 2001
  Secretary of the Interior Order No. 3285A1
    Renewable Energy Development
    Signed by Ken Salazar on February 22, 2010
Notes: Section 211 of Energy Policy Act of 2005
The Secretary of the Interior should in the next 10 years have approved non-hydropower renewable energy projects on the public lands with a generation capacity of at least 10,000 megawatts of electricity.
Executive Order 13212 – Signed by George W. Bush on May 18, 2001
For energy-related projects, agencies shall expedite their review of permits while maintaining safety, public health, and environmental protections.
Secretary of the Interior Order No. 3285A1 – Signed by Ken Salazar on February 22, 2010
Renewable Energy Development by the Department of the Interior
Creates Departmental Task Force on Energy and Climate Change
Sets the production, development, and delivery of renewable energy as one of the Department’s highest priorities.
Instructs agencies and bureaus within the Department to work with each other and other federal agencies, departments, states, local communities, and private landowners to encourage the timely and responsible development of renewable energy.

## Slide 4: Active Applications 2010
BLM-Administered Lands and Active Solar Facility Applications in the Six-State Area
Notes: This map shows all the active applications as of 2010 for solar energy developments on public land. It’s a lot, which is why they decided to do a Programmatic EIS.

## Slide 5: Objectives
Facilitating near-term utility-scale solar energy development on public lands;
Minimizing potential negative environmental, social, and economic impacts;
Providing flexibility to consider a variety of solar energy projects (location, facility size, technology, and so forth);
Optimizing existing transmission infrastructure and corridors; and
Standardizing and streamlining the authorization process for utility-scale solar energy development on BLM lands.
Notes: Facilitating utility-scale solar energy development on public land;
Minimizing negative impacts;
Providing flexibility to consider a variety of projects
Optimizing existing transmission infrastructure
Streamlining the authorization process

## Slide 6: Alternatives
2
3
Solar Energy Development Alternative
  - Excludes certain types of land from development - Identifies and prioritizes Solar Energy Zones
  - Developers could seek variances outside SEZs
1
No Action Alternative
Solar Energy Zones Alternative
  - Projects could be done only in Solar Energy Zones
  - All other land is excluded
Notes: Solar Energy Development Alternative
  Excludes certain types of land from development – 79 million acres
  Identifies and prioritizes Solar Energy Zones – 285,000 acres
  Developers could seek variances outside SEZs – 19 million acres
Solar Energy Zones Alternative
Projects can only be done in Solar Energy Zones
No Action Alternative
BLM continues to approve projects one at a time

## Slide 7: Exclusions Areas (Hannah)
Lands with slopes of greater than 5% determined through GIS analysis
Lands with solar insolation levels less than 6.5 kWh/m2/day determined through National Renewable Energy Laboratory
All Areas of Critical Environmental Concern (ACECs) identified in applicable land use plans
All designated and proposed critical habitat areas for species protected under the Endangered Species Act of 1973
Developed recreational facilities, special-use permit recreation sites (e.g., ski resorts and camps), and all Special Recreation Management Areas
32 categories totaling 79 million acres:
Notes: These are the first five categories for land exclusions
Slopes greater than 5%
Solar insolation levels less than 6.5 kWh per meter squared per day
All Critical Environmental Areas of Concern excluded
All designated and proposed critical habitat for species listed under the ESA
Al areas where there is an applicable land use plan
Hannah Sargel has more information about this for Q and A

## Slide 8: 17 Solar Energy Zones (SEZs)
Solar Energy Zones add up to 285,000 acres
Notes: Started with 24 solar energy zones, 685,000 acres
Cut that back substantially as a result of public comment periods

## Slide 9: Gillespie, Arizona

## Slide 10: Riverside East, California

## Slide 11: DeTilla Gulch, Colorado

## Slide 12: Afton, New Mexico

## Slide 13: Dry Lake, Nevada

## Slide 14: Wah Wah Valley, Utah

## Slide 15: Affected Environment: Geology
Pacific Border and the Lower California provinces
Cascade-Sierra Mountains province
Basin and Range province
Columbia-Snake River Plateau
Colorado Plateau
Middle and Southern Rocky Mountains provinces
Wyoming Basin
Great Plains province
Notes: So for the affected environment
The PEIS found 11 physiographic provinces in the six states
Of those, most of the Solar Energy Zones are in the big U around the Colorado plateau
Basin and Range
Southern Rocky Mountains

## Slide 16: Affected Environment: Water
14 major aquifers
  Basin and Range
  Colorado Plateau
  Central Valley
  Rio Grande
  High Plains
Notes: The watersheds follow the same U around the Colorado Plateau.
The Solar Energy Zones are mainly in
Basin and Range
Rio Grande

## Slide 17: Affected Environment: Wildlife
Amphibians/ Reptiles
Frogs
Toads
Birds
Waterfowl – ducks, geese, swans, herons, cranes, plovers
Mammals
Elk
Salamanders
Turtles
Snakes
Lizards
Mule deer
White-tailed deer
Pronghorn
Bighorn sheep
Black bear
Cougar
Small mammals – rabbits, fox, beaver, skunk
Migratory – warblers, sparrows, swallows, finches
Birds of prey - owls, hawks, vultures, eagles

## Slide 18: Special Status Species (Brinda)
In Solar Energy Zones
  614 plant species
  139 invertebrate species
  84 fish species
  32 amphibian species
  59 reptile species
  123 bird species
  108 mammal species
Total ESA, BLM, State
May affect but not adversely - 6
  1 fish species
  4 bird species
  1 mammal (Utah prairie dog)
Likely to adversely affect - 17
  7 plant species
  1 invertebrate species
  8 fish species
  1 reptile (desert tortoise)
Affected species
Notes: Brinda Bhatt has more information about this topic
Special status species are species listed under:
Endangered Species Act
  Endangered
  Threatened
  Candidates
BLM listing of sensitive species
State listings
Rare species
  State species of concern
  US Fish and Wildlife species of concern
Most will not likely be affected due to
Land exclusions
Design features
Review processes
BLM’s Biological Assessment found:
6 species might be affected but not adversely
17 species likely adversely affected

## Slide 19: Species: Alternatives Analysis
Text | No Action Alternative | Solar Energy Program | Solar Energy Zones
ESA Endangered | 118 | 70 | 12
ESA Threatened | 58 | 35 | 8
ESA Proposed | 3 | 2 | 0
ESA Candidate | 29 | 20 | 7
ESA In Review | 35 | 32 | 26
BLM Sensitive | 654 | 420 | 146
State Listed | 420 | 311 | 75
Rare | 1085 | 723 | 344
TOTAL | 1153 | 777 | 358
Note: The total number of species within each alternative area does not equal the sum across status categories because many species have more than one status listing

## Slide 20: Affected Environment: Climate
Temperature
  Average: mid-40s to mid-70s F
  Range: 10.8° F in Elko, Nev., to 105.6° F in Phoenix
Precipitation
  Rain: 4 inches in Las Vegas to 3 feet in Redding, Calif.
  Snow: 0 in Los Angeles to 5 feet in Denver
Weather
California is largest emitter of CO2 – 52% of six-state total
Six-state emissions are 12.7% of total U.S. CO2 emissions
U.S. CO2 emissions are 21% of worldwide total
Six-state emissions are 2.7% of worldwide total
Carbon Emissions

## Slide 21: Impacts: Vegetation
Development would require total removal of vegetation
  Direct effects
    Increased risk of invasive species
    Changes in species composition and distribution
    Damage to soil crusts
  Indirect effects
    Dust deposits
    Altered drainage
    Runoff
  Mitigation
    Design features can reduce
    Exclusions can avoid
Amargosa niterwort Photo: Amargosa Conservancy

## Slide 22: Impacts: Wildlife
Numerous species affected by
  Loss of habitat
  Disturbance
  Loss of food and prey species
  Loss of breeding areas
  Effects on movement and migration
  Introduction of new species
  Habitat fragmentation
  Changes to water availability
Mitigation
  Design features can reduce
  Exclusions can avoid key areas
Utah prairie dogs Photo: National Park Service

## Slide 23: Impacts: Special Status Species
Same problems as non-status species, but small population makes them more vulnerable
  Habitat fragmentation
  Habitat degradation
  Human disturbance
  Mortality
  Loss of genetic diversity
Most can be mitigated
  Critical habitat excluded
  5.9 million acres
Difficult to mitigate
  Habitat fragmentation
  Clearing vegetation
Desert tortoise Photo: Red Cliffs Desert Reserve

## Slide 24: Impacts: Climate
Adversely affected by dust and vehicle emissions during construction
Local and temporary
Can be mitigated
Air Quality
Each MWh of solar energy produced displaces 1,578 lb. CO2 emissions per year
400 MW solar energy facility at 20% capacity
  Avoids .21% CO2 emissions from electric power facilities
Carbon Emissions

## Slide 25: Impacts: Socioeconomic (Makenna)
Expenditures on wages and salaries
Procurement of goods and services required for construction and operation
Collection of state sales and income taxes
Direct
Influx of workers and their families would affect
  Rental housing
  Public services
  Local government employment
In-migration
Circulation through the economy of:
  Project wages and salaries
  Procurement expenditures
  Tax revenues
Indirect
Notes: Makenna Dunlap has more information about this

## Slide 26: Impacts: Jobs
 | Arizona | California | Colorado | Nevada | New Mex | Utah
Recreation (lost) | -1879 | -12,114 | -1967 | -1827 | -627 | -809
 | -3758 | -24,229 | -3933 | -3653 | -1253 | -1617
Transmission Lines (per 25 miles) | 69 | 72 | 74 | 68 | 77 | 79
 | 158 | 167 | 170 | 157 | 178 | 181
Parabolic Trough (per facility) | 894 | 1935 | 833 | 909 | 682 | 844
 | 3577 | 7740 | 3332 | 3635 | 2728 | 3377
Power Tower (per facility) | 433 | 977 | 403 | 404 | 330 | 409
 | 1732 | 3748 | 1614 | 1616 | 1321 | 1625
Dish Engine (per facility) | 18 | 38 | 16 | 16 | 13 | 17
 | 1319 | 2855 | 1228 | 1230 | 1004 | 1244
Photovoltaic (per facility) | 8 | 18 | 8 | 8 | 6 | 8
 | 615 | 1331 | 573 | 573 | 468 | 580
Notes: Some jobs lost through loss of use of some recreation areas
But a lot of jobs gained
These figures and low and high estimates
Transmission lines – every 25 miles
Then four types of solar facilities – Jobs are per facility
Parabolic Trough and Power Tower facilities create the most jobs
The more facilities are built, the more jobs are created

## Slide 27: Solar facility types
Parabolic Trough
Dish Engine
Power Tower
Photovoltaic (PV)
Notes: Parabolic trough – creates the most jobs
Curved panels
Heat up water in pipes
Power tower – also creates a lot of jobs
Mirrors reflect energy to a tower
Dish Engine
Shaped like a satellite dish
Photovoltaic or PV
Regular solar panels

## Slide 28: Timeline of events
2008
2009
2010
2011
2012
2013
2014
2015
First scoping period May–July 2008
Supplemental Draft PEIS October 28, 2011
Final PEIS
July 27, 2012
Record of Decision October 2012
Second scoping period June 2009
Draft PEIS
Dec. 17, 2010
Notice of Intent May 29, 2008
First projects approved June 9, 2015

## Slide 29: Public Involvement (Stacey)
Supplement Draft PEIS
October 28, 2011
90 days to comment
Final PEIS
July 27, 2012
Record of Decision
October 2012
5 public meetings
17 SEZs, 285,000 acres
15 comment letters
134,000 comments
First Scoping Period
May 29 – July 15, 2008
11 public meetings
Second Scoping Period
Started June 30, 2009
Draft PEIS
December 17, 2010
15,900 comments
24 SEZs, 677,000 acres
300 comments
14 public meetings
86,000 comments
134 days to comment
Notes: Stacey Silverii has more information
Scoping process
First scoping period May 29, 2008 through July 15, 2008
  BLM held 11 public meetings in six states
  Comments collected online and by mail
  15,900 individuals, organizations, and government agencies commented
Second scoping period starting June 30, 2009
  Comments solicited on 24 proposed Solar Energy Zones / 677,000 acres
  300 entities provided comments
Draft PEIS
Published December 17, 2010
Comment period open 134 days
BLM held 14 public meetings in six states
86,000 comments received
Supplement Draft PEIS
Published October 28, 2011
Comment period open 90 days until January 27, 2012
BLM held 5 public meetings
134,000 comments received
Final PEIS
Published July 27, 2012
Solar Energy Zones reduces to 17 SEZs / 285,000 acres
BLM received 15 comment letters from
  county officials
  nongovernmental organizations
  solar energy developers
  solar energy industry associations
  utility representatives
  state and Federal agencies
  tribes
Used those to make clarifications and modifications in ROD
Record of Decision - October 2012

## Slide 30: Decision
Preferred Alternative
  Solar Energy Development
Environmentally Preferred Alternatives
  Solar Energy Development
  Solar Energy Zones
Decision
  Solar Energy Development

## Slide 31: Where are we now? (Mikhail)
State | SEZ | Name | MW | Type | Status
Arizona | Brenda | Quartzite | 100 | tower | operational
 |  | Little Horn | 1000 | trough | pending
 | Gillespie | Sonoran | 300 | trough | pending
Note: 1 MW can power about 1000 homes
Notes: Mikhail Yathnitskiy has more information about this in Q and A
Arizona
1 operational
2 pending
All 3 in a Solar Energy Zone

## Slide 32: Where are we now? (Mikhail)
State | SEZ | Name | MW | Type | Status
California | Riverside East | McCoy | 750 | PV | operational
 |  | Blythe | 485 | PV | operational
 |  | Genesis | 250 | trough | operational
 |  | Desert Harvest | 150 | PV | operational
 |  | Desert Quartzite | 700 | PV | pending
 |  | Sonoran West | 450 | PV | pending
 | Outside SEZ | Desert Sunlight | 550 | PV | operational
 |  | Ivanpah 2 | 370 | tower | operational
 |  | Stateline | 300 | PV | operational
 |  | Ocotillo Sol | 20 | PV | operational
 |  | Soda Mountain | 287 | PV | approved
Notes: California
8 operational
3 pending
6 in a Solar Energy Zone
5 outside a Solar Energy Zone

## Slide 33: Where are we now? (Mikhail)
State | SEZ | Name | MW | Type | Status
Nevada | Dry Lake | Dry Lake Zone | 200 | PV | operational
 |  | Dry Lake Center | 130 | PV | operational
 |  | Harry Allen Solar | 112 | PV | operational
 |  | Silver State North | 50 | PV | operational
 |  | Silver State South | 350 | PV | operational
 | Millers | Crescent Dunes | 110 | tower | operational
 | Outside SEZ | Luning | 50 | PV | approved
Notes: Nevada
6 operational
1 approved
All operational facilities in a Solar Energy Zone

## Slide 34
Questions
  What kind of land was excluded from solar energy development? (Hannah Sargel)
  How does the project affect endangered and rare species? (Brinda Bhatt)
  Did the EIS discuss socioeconomic impacts? What were they? (Makenna Dunlap)
  Did the public get a chance to comment on this project? How many comments did they get? (Stacey Silverii)
  Where is this project now? Were any site-specific solar energy facilities approved? (Mikhail Yakhnitskiy)